## Slide 1
FLUME TEST ARTICLES · 4-BUOY CLUSTER
How much payload can the cluster carry?
A mass on the hub, moved around: the stability envelope and the physics behind it
Payload-stability study · 2026-10-14 · Capytaine hydrostatics, large-angle statics, FloatSim cross-check
Notes: This deck answers one question: how much mass can sit on top of the 4-buoy cluster, and where, before its stability is compromised. Every number comes from the study's records; the drawings are to scale and come from the solved equilibria. The animations play in PowerPoint's slide show.

## Slide 2
The bottom line
Payload on the hub, free-floating in calm water, hub free to tilt, pins kept dry
54.7 kg
centred mass until all four pins reach the waterline: the cluster only sinks
0.6 kg·m
mass × offset that tilts the hub 5°, in every direction: the hub is a seesaw
Never
do the buoys flop on their gimbals: margin ≥ 24 N·m/rad at every load
30–85°
of hub tilt when an off-centre limit is reached: use a tilt limit to operate
What limits the cluster
Centred: reserve buoyancy. Each kg sinks it 12.6 mm; at 54.7 kg the spar tops and pins are awash.
Off-centre, up to ~0.3 m: the first pin goes awash, e.g. 36.9 kg at 0.1 m or 27.8 kg at 0.2 m towards a buoy.
Off-centre, beyond ~0.3 m: the hub rolls onto its side at mass × offset ≈ 6.8 kg·m; buoys may touch first.
For operation: ≤ 10° of hub tilt ↔ mass × offset ≤ 1.2 kg·m.
Notes: Four numbers carry the story. A centred mass only sinks the cluster: 54.7 kg puts all four pins at the waterline. Off-centre, the hub rocks like a seesaw on buoys that stay upright; every 0.6 kg·m of mass times offset gives about 5 degrees of hub tilt, in any direction. The buoys never flop over on their gimbals. And every limit is reached at 30 to 85 degrees of hub tilt, so in practice an allowable tilt is the better operating limit.

## Slide 3
The cluster and the question
Four buoys hung from a hub on gimbals; a mass on the hub, moved parallel to the waterline
The question
How much mass can sit on the hub, and how far from the centre, before stability is compromised? Then: an envelope of mass and centre of gravity.
The set-up
Mass: a point mass on the hub, in the pin plane (+0.717 m), moved horizontally up to 0.5 m.
Water: calm; the cluster free-floating (no mooring).
Hub: free to tilt on the gimbals, with no mechanical stop.
Limit: loss of restoring, or a pin reaching the water.
Cluster: 88.1 kg unloaded: 4 × 21.52 kg buoys + 2 kg hub.
Notes: The cluster is four OSU buoys hung from a small hub by gimbals at the spar tops, 0.717 m above the water. The gimbals leave roll and pitch free, so each buoy can stay vertical whatever the hub does. The study puts a point mass on the hub, in the pin plane, and moves it horizontally. The decisions: free-floating, calm water, the hub free to tilt, and the pins must stay dry.

## Slide 4
How it was computed
FloatSim's restoring is fixed at one draft and valid to ~5.7°: the limits lie far beyond both
1 Capytaine at every draft
The buoy re-meshed sunk −0.95 … +0.72 m: buoyancy, pin load and tilt stiffness at each draft (36 panels round; 96 reproduces the record's 74.08 N·m/rad).
2 Large-angle statics
Rigid hub on four buoys that hang vertically from their pins. The equilibrium at any tilt minimises the potential energy; its stiffness and each buoy's gimbal margin decide stability.
3 FloatSim cross-check
FloatSim's own cluster model, solved statically with its joints, against the statics at small tilt: identical sinkage, tilt within 0.002°.
Why not FloatSim alone: its restoring does not change as the cluster sinks (Level 2 is not wired), its kinematics are small-angle, and its linear model has no weight to load the joints. An approved exception to the 'use FloatSim' rule, with FloatSim checking the small-angle range.
Notes: FloatSim can't reach these limits on its own: its restoring is a constant matrix fixed at one draft, it is only valid to about 5.7 degrees, and its linear model never loads the joints with the hub's weight. So the buoy's hydrostatics were computed with Capytaine at every draft, the cluster was solved exactly at any tilt with those hydrostatics, and FloatSim's own static solve was used to check the small-angle range, where the two agree exactly.

## Slide 5
What one buoy feels as it sinks
The pin load grows linearly; the buoy's own restoring outgrows the tipping effect of that load
Chart: Extra buoyancy: 194 N/m until the spar top goes under
| 0.0 | 0.025 | 0.05 | 0.075 | 0.1 | 0.125 | 0.15 | 0.175 | 0.2 | 0.225 | 0.25 | 0.275 | 0.3 | 0.325 | 0.35 | 0.375 | 0.4 | 0.425 | 0.45 | 0.475 | 0.5 | 0.525 | 0.55 | 0.575 | 0.6 | 0.625 | 0.65 | 0.675 | 0.7 | 0.71 | 0.715
pin load holding the sinkage (N) | 0 | 4.8515 | 9.703 | 14.5545 | 19.406 | 24.2575 | 29.109 | 33.9606 | 38.8121 | 43.6636 | 48.5151 | 53.3666 | 58.2181 | 63.0696 | 67.9211 | 72.7726 | 77.6241 | 82.4756 | 87.3271 | 92.1786 | 97.0302 | 101.8817 | 106.7332 | 111.5847 | 116.4362 | 121.2877 | 126.1392 | 130.9907 | 135.8422 | 137.7828 | 138.7531
Chart: Gimbal stability of one buoy
| 0.0 | 0.025 | 0.05 | 0.075 | 0.1 | 0.125 | 0.15 | 0.175 | 0.2 | 0.225 | 0.25 | 0.275 | 0.3 | 0.325 | 0.35 | 0.375 | 0.4 | 0.425 | 0.45 | 0.475 | 0.5 | 0.525 | 0.55 | 0.575 | 0.6 | 0.625 | 0.65 | 0.675 | 0.7 | 0.71 | 0.715
buoy's restoring, C55 | 73.7532 | 78.2142 | 82.7965 | 87.5 | 92.3248 | 97.2709 | 102.3383 | 107.527 | 112.837 | 118.2683 | 123.8208 | 129.4946 | 135.2898 | 141.2062 | 147.2439 | 153.4029 | 159.6832 | 166.0847 | 172.6076 | 179.2517 | 186.0171 | 192.9039 | 199.9119 | 207.0411 | 214.2917 | 221.6636 | 229.1567 | 236.7712 | 244.5069 | 247.6352 | 249.2066
tipping by the pin load, P × 1.62 m | 0 | 7.8788 | 15.7577 | 23.6365 | 31.5154 | 39.3942 | 47.2731 | 55.1519 | 63.0308 | 70.9096 | 78.7885 | 86.6673 | 94.5462 | 102.425 | 110.3039 | 118.1827 | 126.0616 | 133.9404 | 141.8193 | 149.6981 | 157.577 | 165.4558 | 173.3347 | 181.2135 | 189.0924 | 196.9712 | 204.8501 | 212.7289 | 220.6078 | 223.7593 | 225.3351
net margin | 73.7532 | 70.3354 | 67.0388 | 63.8634 | 60.8094 | 57.8767 | 55.0652 | 52.3751 | 49.8062 | 47.3586 | 45.0323 | 42.8273 | 40.7436 | 38.7812 | 36.94 | 35.2201 | 33.6216 | 32.1443 | 30.7883 | 29.5536 | 28.4402 | 27.448 | 26.5772 | 25.8276 | 25.1994 | 24.6924 | 24.3067 | 24.0423 | 23.8992 | 23.8759 | 23.8715
Reserve: 139 N per buoy before its pin is awash → 54.7 kg on the hub. The net gimbal margin never drops below 24 N·m/rad: the buoys stay upright at every load.
Notes: What one buoy feels as the hub pushes it down. Left: the extra buoyancy grows in a straight line, 194 newtons per metre, because the spar's cross-section is constant, until the spar top goes under at 0.717 m; that caps each buoy at about 139 newtons, 56.8 kg for the four including the hub. Right: why the buoy doesn't flop over on its gimbal. The pin load at the top tries to tip it (red), but the buoy's own restoring grows faster as it sinks (blue), because the new buoyancy is added near the waterline. The margin (green) never drops below 24 N·m/rad.

## Slide 6
A centred mass only sinks the cluster
All four buoys share the load; nothing tilts
12.6 mm
of sinkage per kg of payload (194 N/m per buoy, four buoys)
54.7 kg
on the hub puts the spar tops and pins at the waterline
0°
hub tilt: a centred mass never tips the cluster
Notes: Scenario one: the mass in the centre. Nothing tilts; the four buoys share the load equally and the cluster sinks 12.6 mm per kilogram. The hub's own 2 kg already sinks it 25 mm. At 54.7 kg the spar tops, and the pins with them, reach the waterline. That is the centred limit: the cluster runs out of reserve buoyancy, it does not capsize.

## Slide 7
Off-centre, the hub rocks like a seesaw
0.2 m towards a buoy: the buoys stay upright; only their difference in sinkage resists the tilt
67 N·m/rad
hub tilt stiffness: buoy sinkage × buoy distance² (0.42 m from the centre)
3 kg → 5°
at 0.2 m: a few kilograms tilt the hub visibly
27.8 kg
first pin awash, hub at 54° tilt
Notes: Scenario two: the mass 0.2 m from the centre, towards one buoy. The hub rocks like a seesaw. The buoys stay vertical on their gimbals; the loaded buoy sinks, the far one barely moves, and only that difference in sinkage resists the tilt. That resistance is small, 67 N·m per radian, because the buoys are only 0.42 m from the centre. 3 kg already tilts the hub 5 degrees; at 27.8 kg the loaded pin reaches the water with the hub at 54 degrees.

## Slide 8
The tilt depends only on mass × offset
Every branch, in every direction, falls on one curve
Chart: Hub tilt against payload moment: 12 branches
0.50 m, 0° | 0 | 1.0423 | 2.085 | 3.1284 | 4.1728 | 5.2186 | 6.2661 | 7.3158 | 8.3679 | 9.4229 | 10.4811 | 11.5429 | 12.6088 | 13.6791 | 14.7543 | 15.8349 | 16.9212 | 18.0139 | 19.1134 | 20.2202 | 21.335 | 22.4584 | 23.5909 | 24.7332 | 25.8862 | 27.0505 | 28.2271 | 29.4167 | 30.6205 | 31.8394 | 33.0747 | 34.3275 | 35.5993 | 36.8917 | 38.2064 | 39.5452 | 40.9104 | 42.3044 | 43.7299 | 45.1902 | 46.6891 | 48.2307 | 49.8202 | 51.4638 | 53.1689 | 54.9446 | 56.8025 | 58.7574 | 60.8292 | 63.0448 | 65.4436 | 68.0857 | 71.0733 | 74.6065 | 79.2089
0.50 m, 45° | 0 | 1.0423 | 2.085 | 3.1284 | 4.1728 | 5.2186 | 6.2661 | 7.3158 | 8.3679 | 9.4229 | 10.4811 | 11.5429 | 12.6088 | 13.6791 | 14.7543 | 15.8349 | 16.9212 | 18.0139 | 19.1134 | 20.2202 | 21.335 | 22.4584 | 23.5909 | 24.7332 | 25.8862 | 27.0505 | 28.2271 | 29.4167 | 30.6205 | 31.8394 | 33.0747 | 34.3275 | 35.5993 | 36.8917 | 38.2064 | 39.5452 | 40.9104 | 42.3044 | 43.7299 | 45.1902 | 46.6891 | 48.2307 | 49.8202 | 51.4638 | 53.1689 | 54.9446 | 56.8025 | 58.7574 | 60.8292 | 63.0448 | 65.4436 | 68.0857 | 71.0733 | 74.6065 | 79.2089
Reading it
Hub tilt | mass × offset | e.g. at 0.2 m
2° | 0.24 kg·m | 1.2 kg
5° | 0.60 kg·m | 3.0 kg
10° | 1.19 kg·m | 6.0 kg
20° | 2.35 kg·m | 11.8 kg
30° | 3.44 kg·m | 17.2 kg
Lines: 12 branches, offsets 0.05–0.5 m, between buoys (teal) and towards a buoy (red): they lie on top of each other, each ending at its own limit. Dashed: the small-angle formula.
Notes: Why one number describes the tilt. Every branch, at six offsets and in two directions, falls on one curve when plotted against mass times offset: the payload's moment is what tilts the hub, and the hub's resistance is the same in every direction because the square of buoys is symmetric. For small tilts the curve follows theta equals m g e over 67 N·m per radian (dashed); at larger tilts it bends because the lever arms shorten as the hub turns.

## Slide 9
Far out, the hub rolls onto its side
0.4 m between buoys: no pin reaches the water before the hub turns over
6.8 kg·m
mass × offset at which the hub rolls onto its side, in every direction
17.1 kg
at 0.4 m; the lowest pin is still 182 mm above water
15.0 kg
at 0.4 m the buoys may already touch each other
Notes: Scenario three: the mass 0.4 m out, between two buoys, near the edge of the cluster. Here the hub keeps tilting long before any pin reaches the water, and rolls onto its side: beyond about 85 degrees the payload is no longer on top. That happens at a mass times offset of about 6.8 kg·m in every direction. Before that, as the hub turns, the hanging buoys swing towards each other and may touch.

## Slide 10
Watch it happen
The mass rising from zero to the limit (animations play in slide show)
Centred
0.2 m towards a buoy
0.4 m between buoys
Notes: The three loadings animated, the mass rising from zero to the limit. They play in slide show (and in normal view in recent PowerPoint). Watch the centred cluster sink straight down, the seesaw tilt with the buoys hanging vertically, and the hub roll over when the mass is far out.

## Slide 11
The payload envelope
Payload mass against its offset from the hub centre: limits (solid) and hub tilt (dashed)
Chart: payload offset from the hub centre (m)
| 0.0 | 0.025 | 0.05 | 0.075 | 0.1 | 0.125 | 0.15 | 0.175 | 0.2 | 0.225 | 0.25 | 0.275 | 0.3 | 0.325 | 0.35 | 0.375 | 0.4 | 0.425 | 0.45 | 0.475 | 0.5
limit, 0° (between buoys) | 54.6784 | 50.4688 | 46.7455 | 43.6406 | 40.875 | 38.4453 | 36.2321 | 34.3516 | 32.6094 | 30.4219 | 27.375 | 24.8906 | 22.8125 | 21.0625 | 19.5547 | 18.25 | 17.1094 | 16.1016 | 15.2109 | 14.4062 | 13.6875
limit, 15° | 54.6784 | 49.5112 | 45.2565 | 41.6694 | 38.5665 | 35.9818 | 33.6404 | 31.5941 | 29.7982 | 28.2509 | 26.9844 | 24.8906 | 22.8125 | 21.0625 | 19.5547 | 18.25 | 17.1094 | 16.1016 | 15.2109 | 14.4062 | 13.6875
limit, 30° | 54.6784 | 48.9989 | 44.3381 | 40.5289 | 37.3023 | 34.5581 | 32.2498 | 30.1498 | 28.3086 | 26.7533 | 25.278 | 24.0108 | 22.8125 | 21.0625 | 19.5547 | 18.25 | 17.1094 | 16.1016 | 15.2109 | 14.4062 | 13.6875
limit, 45° (towards a buoy) | 54.6784 | 48.7803 | 44.0457 | 40.2047 | 36.9412 | 34.132 | 31.7634 | 29.7165 | 27.8341 | 26.2622 | 24.7947 | 23.5246 | 22.3436 | 21.0625 | 19.5547 | 18.25 | 17.1094 | 16.1016 | 15.2109 | 14.4062 | 13.6875
hub tilt 5° | 23.9557 | 11.9778 | 7.9852 | 5.9889 | 4.7911 | 3.9926 | 3.4222 | 2.9945 | 2.6617 | 2.3955 | 2.1778 | 1.9963 | 1.8427 | 1.7111 | 1.597 | 1.4972 | 1.4091 | 1.3308 | 1.2608 | 1.1978
hub tilt 10° | 47.729 | 23.8645 | 15.9097 | 11.9322 | 9.5458 | 7.9548 | 6.8184 | 5.9661 | 5.3032 | 4.7729 | 4.339 | 3.9774 | 3.6714 | 3.4092 | 3.1819 | 2.983 | 2.8075 | 2.6515 | 2.512 | 2.3864
hub tilt 20° | 31.3359 | 23.502 | 18.8015 | 15.6679 | 13.4296 | 11.751 | 10.4452 | 9.4007 | 8.5461 | 7.8339 | 7.2313 | 6.7148 | 6.2671 | 5.8753 | 5.5298 | 5.2226 | 4.9476 | 4.7003
buoys may touch (worst direction) | 45.6022 | 40.8289 | 36.9636 | 33.7653 | 31.0697 | 28.7801 | 26.6601 | 23.995 | 21.8126 | 19.9958 | 18.4568 | 17.1375 | 15.9966 | 14.9968 | 14.1125 | 13.3284 | 12.6264 | 11.9975
Reading it
Below a solid line: stable and pins dry, for that direction.
Worst direction: towards a buoy (red), by up to 15 %.
Up to ~0.3 m: a pin goes awash. Beyond: the hub rolls over.
Dashed: hub tilt 5° (darkest), 10°, 20° (lightest), far inside the limits.
Dotted: buoys may touch, before the limit beyond ~0.2 m.
Notes: The envelope. Each solid line is the payload limit for one direction of the offset: pins awash at small offsets, the hub rolling over beyond about 0.3 m. Towards a buoy (red) is the worst direction, by up to 15 percent. The dashed lines are hub tilts of 5, 10 and 20 degrees: they lie far inside the limits, which is why a tilt limit is the practical operating envelope. The dotted line is where the buoys may touch, which comes before the limit at large offsets.

## Slide 12
Mass and CG envelope of the whole cluster
Total mass against the horizontal offset of the cluster's CG (unloaded 88.1 kg, level geometry)
Chart: horizontal offset of the cluster's CG (mm)
| 0.0 | 9.106677252591597 | 17.335547804139246 | 24.84840073450912 | 31.69710364080494 | 37.9818391082812 | 43.719093074683336 | 49.10109219181124 | 54.038518303703206 | 57.7621398395595 | 59.27634143172665 | 60.590280659242175 | 61.71517460603738 | 62.719037038733774 | 63.586756128223065 | 64.36330292485658 | 65.06122885510062 | 65.68498204756719 | 66.26836817121541 | 66.76962763297516 | 67.24887611467315
limit, 0° (between buoys) | 142.7584 | 138.5487 | 134.8255 | 131.7206 | 128.955 | 126.5253 | 124.3121 | 122.4316 | 120.6894 | 118.5019 | 115.455 | 112.9706 | 110.8925 | 109.1425 | 107.6347 | 106.33 | 105.1894 | 104.1816 | 103.2909 | 102.4862 | 101.7675
limit, 45° (towards a buoy) | 142.7584 | 136.8603 | 132.1257 | 128.2847 | 125.0212 | 122.212 | 119.8434 | 117.7965 | 115.9141 | 114.3422 | 112.8747 | 111.6046 | 110.4236 | 109.1425 | 107.6347 | 106.33 | 105.1894 | 104.1816 | 103.2909 | 102.4862 | 101.7675
hub tilt 5° | 112.0357 | 100.0578 | 96.0652 | 94.0689 | 92.8711 | 92.0726 | 91.5022 | 91.0745 | 90.7417 | 90.4755 | 90.2578 | 90.0763 | 89.9227 | 89.7911 | 89.677 | 89.5772 | 89.4891 | 89.4108 | 89.3408 | 89.2778
hub tilt 10° | 135.809 | 111.9445 | 103.9897 | 100.0122 | 97.6258 | 96.0348 | 94.8984 | 94.0461 | 93.3832 | 92.8529 | 92.419 | 92.0574 | 91.7514 | 91.4892 | 91.2619 | 91.063 | 90.8875 | 90.7315 | 90.592 | 90.4664
hub tilt 20° | 119.4159 | 111.582 | 106.8815 | 103.7479 | 101.5096 | 99.831 | 98.5252 | 97.4807 | 96.6261 | 95.9139 | 95.3113 | 94.7948 | 94.3471 | 93.9553 | 93.6098 | 93.3026 | 93.0276 | 92.7803
At the limit
Payload at | Total mass | CG offset
0.0 m | 142.8 kg | 0 mm
0.1 m | 125.0 kg | 30 mm
0.2 m | 115.9 kg | 48 mm
0.3 m | 110.4 kg | 61 mm
0.4 m | 105.2 kg | 65 mm
Worst direction (towards a buoy). The CG offset is that of the whole cluster with the payload, before it tilts.
Notes: The same envelope expressed as the whole cluster's mass and centre of gravity, which is how a loading envelope is usually given. The cluster weighs 88 kg unloaded. Moving its overall centre of gravity just a few millimetres off-centre tilts the hub: about 7 mm for 5 degrees with a light payload. The limits need tens of millimetres.

## Slide 13
Cross-checks
Capytaine against the record; FloatSim against the large-angle statics at small tilt
74.08
N·m/rad: the buoy's pitch stiffness on the 96-panel mesh = the record (DESIGN-BASIS §C8)
0.002°
largest tilt difference between FloatSim and the statics (2 kg at 0.2 m)
Payload | Offset, direction | FloatSim sinkage / tilt | Statics sinkage / tilt | Agree
2 kg | 0.00 m, 0° | 52.6 mm / 0.000° | 52.6 mm / 0.000° | yes
10 kg | 0.00 m, 0° | 157.9 mm / 0.000° | 157.9 mm / 0.000° | yes
1 kg | 0.10 m, 0° | 39.5 mm / 0.869° | 39.5 mm / 0.869° | yes
1 kg | 0.10 m, 45° | 39.5 mm / 0.869° | 39.5 mm / 0.869° | yes
2 kg | 0.20 m, 0° | 52.6 mm / 3.475° | 52.6 mm / 3.477° | yes
2 kg | 0.20 m, 30° | 52.6 mm / 3.475° | 52.6 mm / 3.477° | yes
Both on the same 12-panel hydrostatics; sinkage is measured from the unloaded draft and includes the hub's 2 kg.
Notes: How far to trust it. The hydrostatics reproduce the recorded pitch stiffness of the buoy on the fine mesh. And FloatSim, solving its own model of the cluster with its joints, gives the same sinkage and the same tilt as the large-angle statics in the range where FloatSim is valid. The large-angle part rests on simple, exact geometry: vertical buoys of constant section.

## Slide 14
What it means for loading the cluster
Guidance
Keep the mass central. Centred, the cluster carries 54.7 kg before its pins are awash; it only sinks, 12.6 mm per kg.
Plan off-centre loads by hub tilt. 5° ↔ 0.6 kg·m, 10° ↔ 1.2 kg·m, in every direction.
Worst direction: towards a buoy, by up to 15 % on the limit.
Don't rely on the limits for operation: they come at 30–85° of hub tilt, where payload retention, the gimbals and buoy contact govern.
Not included
Waves and dynamics: this is calm-water statics; waves reduce the margins.
The mooring: free-floating; the moored cluster's 1° pretension lean is not included.
A raised payload: a mass above the pin plane adds a tipping moment to the hub; needs a new run.
Hardware: gimbal travel, payload retention and hub buoyancy are not modelled; buoy contact is only flagged.
Notes: What to take away. Keep the payload central: the cluster can then carry tens of kilograms. Off-centre, plan by hub tilt, not by the stability limit, which only comes at extreme tilts. The analysis is static and in calm water; waves, the mooring, a raised payload and the gimbals' real travel would all reduce the margins.

## Slide 15
NEXT
The same envelope for the 2.4 m platform
The 2.4 m platform in the flume (mooring rev D), to scale
Same method: the Capytaine draft table is reused; the statics extend to four hubs and the deck.
New physics: the deck sits at +0.90 m, above the pins, so a mass on it tips the hubs as they tilt, a term that is zero for the cluster.
Then: a check in waves for the loads that matter, if needed.
Notes: Next, the same exercise for the 2.4 m square platform. Its deck sits at 0.90 m, above the pins, so a mass on the deck tips the hubs as they tilt: the term that is zero for the cluster. The statics need that extension; the Capytaine draft table is reused as it is.