## Slide 1
FLUME TEST ARTICLES · 4×4 PLATFORM
How much payload can the platform carry?
A mass on the deck, moved around and raised: the stability envelope and the physics behind it
Payload-stability study · 2026-10-15 · Capytaine hydrostatics, large-angle statics, FloatSim cross-check
Notes: This deck repeats the cluster study for the 2.4 m platform: how much mass can sit on the deck, and where, before its stability is compromised. Every number comes from the study's records; the drawings are to scale and come from the solved equilibria. The animations play in PowerPoint's slide show.

## Slide 2
The bottom line
Payload on the deck, free-floating in calm water, gimbals free, pins kept dry
213 kg
centred until all 16 pins reach the waterline: the platform only sinks
15 kg·m
mass × offset per 5° of deck tilt: 29× stiffer than the cluster's hub
202 kg·m
mass × CG height above the pins that tips the deck, even centred
65 kg
at the deck edge, 1.2 m towards a corner (deck at 24°)
What limits the platform
Centred, on the deck: reserve buoyancy. Each kg sinks it 3.16 mm; at 212.7 kg every pin is awash.
Off-centre: one cluster's four pins go awash together; worst towards a hub, on the diagonal. E.g. 97 kg at 0.6 m, 65 kg at 1.2 m.
Raised payload: keep mass × CG height above the pins below 202 kg·m, or the deck tips over (e.g. 170 kg with its CG 1 m above the deck).
For operation: ≤ 5° of deck tilt ↔ mass × offset ≤ 15 kg·m (≤ 10° ↔ 30 kg·m), for a payload on the deck.
Notes: Four numbers carry the story. A centred mass only sinks the platform: 213 kg puts all sixteen pins at the waterline. Off-centre, the whole deck tilts on its four clusters, and it is about thirty times stiffer than the cluster's hub: about 15 kg·m of mass times offset per 5 degrees. The new physics is height: a payload whose mass times CG height above the pins exceeds about 202 kg·m tips the deck over even when centred. And at the edge, 1.2 m towards a corner, the limit is 65 kg.

## Slide 3
The platform and the question
Four clusters hung from a deck on gimbals; a mass on the deck, moved parallel to the waterline
The question
How much mass can sit on the deck, and how far from the centre, before stability is compromised? Then: an envelope of mass and centre of gravity.
The set-up
Mass: a point mass on the deck frame (+0.90 m), moved horizontally up to 1.2 m; its CG also raised 0.5 and 1.0 m.
Water: calm; the platform free-floating (no mooring).
Gimbals: free, buoys to hubs and hubs to the deck; no stops.
Limit: loss of restoring, or a pin reaching the water.
Platform: 358.3 kg unloaded: 16 × 21.52 kg buoys + 4 × 2 kg hubs + 6 kg deck.
Notes: The platform is the rev D test platform: sixteen OSU buoys on a 0.8 m grid, in four clusters of four. Each buoy hangs from its cluster's hub on a gimbal at the spar top, exactly as in the cluster; each hub hangs from the deck frame on another gimbal, at the hub centre. The deck frame sits 0.18 m above the pins. The study puts a point mass on the deck, moves it horizontally out to the outer buoy line, and also raises its centre of gravity. Same decisions as for the cluster: free-floating, calm water, gimbals free, pins dry.

## Slide 4
How the platform carries a load
The deck rests on four clusters; each cluster acts as one spring
1 Capytaine at every draft
The cluster study's buoy table is reused as it is: buoyancy, pin load and tilt stiffness for sinkage −0.95 … +0.72 m.
2 Large-angle statics
Deck + 4 hubs + 16 hanging buoys, exact at any deck tilt: 11 coordinates, equilibrium at the minimum of potential energy, stability from its stiffness.
3 FloatSim cross-check
FloatSim's own platform model (16 buoys, coupled BEM, joints), solved statically: identical sinkage and tilt at small angles.
Why each hub stays level
The deck's load reaches each hub at its gimbal: the hub centre, in the plane of its four pins. It has no lever arm to tilt the hub, so the hub hangs level and its four buoys sink together.
So each cluster is one vertical spring under the deck: 4 × 194 N/m, 1.13 m from the centre. Only the deck tilts. Checked, not assumed: the hub moment residual is ≤ 2e-14 N·m and the hub tilts are in the stability check.
Notes: How the platform carries a load, and how it was computed. The key simplification is exact, not assumed: each hub receives the deck's load at its own gimbal, which sits at the hub centre in the plane of its four pins. That load has no lever arm to tilt the hub, so the hub hangs level and its four buoys sink together. Each cluster then acts as one vertical spring under the deck, and only the deck tilts. The hub tilts are still in the stability check. The method is the cluster's: the same Capytaine draft table, the statics extended to the deck and four hubs, and FloatSim's own platform model checking the small-angle range.

## Slide 5
A centred mass only sinks the platform
All sixteen buoys share the load; nothing tilts
3.16 mm
of sinkage per kg of payload (194 N/m per buoy, sixteen buoys)
212.7 kg
on the deck puts all sixteen pins at the waterline
≈ 4 × 55 kg
the cluster's centred limit, four times, less the 6 kg deck
Notes: Scenario one: the mass in the centre of the deck. Nothing tilts; the sixteen buoys share the load and the platform sinks 3.16 mm per kilogram, a quarter of the cluster's rate because there are four times the buoys. The deck and hubs alone sink it 44 mm. At 212.7 kg all sixteen pins reach the waterline: about four clusters' worth, less the deck.

## Slide 6
Off-centre, the whole deck tilts
1.2 m towards a corner: the hubs stay level; the clusters' difference in sinkage resists the tilt
1987 N·m/rad
deck tilt stiffness: 29× the cluster's hub (16 buoys at ~0.8 m)
14 kg → 5°
at the corner, 1.2 m out on the diagonal
64.9 kg
the near cluster's pins awash, deck at 24° tilt
Notes: Scenario two: the mass towards a corner, 1.2 m out on the diagonal, the worst direction. The deck tilts as a whole on its four clusters; the hubs stay level, so each cluster's buoys move together. The resistance is the clusters' difference in sinkage times their distance squared: 1987 N·m per radian, thirty times the cluster's hub, because sixteen buoys work at about 0.8 m instead of four at 0.3 m. 14 kg at the corner tilts the deck 5 degrees; at 64.9 kg the near cluster's pins reach the water with the deck at 24 degrees.

## Slide 7
The tilt follows mass × offset
Payload on the deck: one curve; raised a metre: the heavy masses tilt the deck further
Chart: Deck tilt against payload moment, towards a corner
1.2 m, CG 1 m above the deck | 0 | 0.34315 | 0.69038 | 1.0418 | 1.3975 | 1.7575 | 2.122 | 2.4911 | 2.8649 | 3.2434 | 3.6269 | 4.0154 | 4.4091 | 4.8082 | 5.2126 | 5.6227 | 6.0386 | 6.4605 | 6.8885 | 7.3228 | 7.7637 | 8.2114 | 8.666 | 9.128 | 9.5974 | 10.0747 | 10.5601 | 11.0539 | 11.5566 | 12.0684 | 12.5899 | 13.1214 | 13.6635 | 14.2167 | 14.7816 | 15.3589 | 15.9492 | 16.5533 | 17.1722 | 17.8068 | 18.4581 | 19.1276 | 19.8165 | 20.5265 | 21.2595 | 22.0176 | 22.8033 | 23.6198 | 24.4705 | 25.36 | 26.2938
small-angle: θ = m g e / 1987 N·m/rad | 0 | 0.77996 | 1.5599 | 2.3399 | 3.1198 | 3.8998 | 4.6797 | 5.4597 | 6.2396 | 7.0196 | 7.7996 | 8.5795 | 9.3595 | 10.1394 | 10.9194 | 11.6993 | 12.4793 | 13.2592 | 14.0392 | 14.8192 | 15.5991 | 16.3791 | 17.159 | 17.939 | 18.7189 | 19.4989 | 20.2788 | 21.0588 | 21.8388 | 22.6187
Reading it (CG on the deck)
Deck tilt | mass × offset | e.g. at 1.0 m
2° | 6.2 kg·m | 7.0 kg
5° | 15.1 kg·m | 17.3 kg
10° | 30.1 kg·m | 33.9 kg
20° | 60.8 kg·m | 64.6 kg
mass × offset: the smallest over the offsets, so a safe reading; the same in every direction.
Raised payloads tilt further for the same moment: by 1 / (1 − m·H / 202 kg·m), H = CG height above the pins.
Notes: Why mass times offset describes the tilt. With the mass on the deck (red), the branches at three offsets almost fall on one curve: the payload's moment tilts the deck, against the clusters' 1987 N·m per radian. They separate a little because a heavy mass also sits above the pins and helps the tilt along. With the CG raised a metre (purple, dashed) that effect is large: the same moment tilts the deck much more, and most for the heaviest masses.

## Slide 8
A raised payload tips the deck further
CG 1.0 m above the deck, 0.2 m off centre: the raised mass leans out over the low side
112 kg
limit at 0.2 m with the CG 1 m up (on the deck: 164 kg)
23°
deck tilt at that limit (on the deck: 11°)
170 kg
centred, CG 1 m up: the level deck tips over before any pin is awash
Notes: Scenario three, the new physics: the same kind of offset load, but with the payload's centre of gravity a metre above the deck. As the deck tilts, the raised mass moves sideways over the low side and adds to the tipping moment. At 0.2 m off centre the limit falls from 164 kg with the mass on the deck to 112 kg raised, and the deck reaches 23 degrees instead of 11.

## Slide 9
How high can the payload's CG be?
Centred payload: its limit against the height of its CG above the deck
Chart: Centred payload: pins awash, or the deck tips over
| 0.0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1.0 | 1.1 | 1.2 | 1.3 | 1.4 | 1.5 | 1.6 | 1.7 | 1.8 | 1.9 | 2.0
limit (large-angle statics) | 212.9688 | 212.9688 | 212.9531 | 212.9375 | 212.9219 | 212.8906 | 212.8125 | 212.4688 | 204.125 | 185.5312 | 169.875 | 156.6562 | 145.3594 | 135.5625 | 127.0156 | 119.4688 | 112.7812 | 106.7969 | 101.4219 | 96.5625 | 92.1406
tips over: m (h + 0.18 m) = 202 kg·m | 1101.3724 | 865.0264 | 712.1949 | 605.2587 | 526.2432 | 465.4761 | 417.2902 | 378.1448 | 345.7138 | 318.4062 | 295.0969 | 274.9675 | 257.4089 | 241.9582 | 228.2573 | 216.0248 | 205.0368 | 195.1124 | 186.1045 | 177.8916 | 170.3729 | 163.464 | 157.0937 | 151.2012 | 145.7347 | 140.6498 | 135.9077 | 131.475 | 127.3223 | 123.4239 | 119.7571 | 116.3019 | 113.0405 | 109.957 | 107.0373 | 104.2686 | 101.6395 | 99.1398 | 96.76 | 94.4919 | 92.3276
all pins awash | 212.7137 | 212.7137
The rule
mass × CG height above the pins
≤ 202 kg·m
Payload | CG at most above the deck
100 kg | 1.83 m
150 kg | 1.16 m
200 kg | 0.82 m
Why: a raised mass moves sideways as the deck tilts; past this, its tipping moment beats the clusters' 1987 N·m/rad.
A stability limit, not a working value: near it, small offsets give large tilts.
Notes: How high can the payload's centre of gravity be? With the mass centred, the pins limit it to 213 kg while the CG is low. Above about 0.76 m over the deck, the level deck tips over first. Tilting the deck by a small angle moves a mass at height H above the pins sideways by H times the angle: a tipping moment m g H per radian, against the clusters' 1987. They balance at m times H equal to 202 kg·m, the dashed curve, which the full calculation follows exactly.

## Slide 10
Watch it happen
The mass rising from zero to the limit (animations play in slide show)
Centred, on the deck
1.2 m towards a corner
CG 1 m up, 0.2 m off centre
Notes: The three loadings animated, the mass rising from zero to the limit. They play in slide show (and in normal view in recent PowerPoint). Watch the centred platform sink straight down, the deck tilt towards the loaded corner with the hubs staying level, and the raised mass lean out over the low side.

## Slide 11
The payload envelope
Payload mass against its offset from the deck centre: limits (solid), raised CG (purple) and deck tilt (dashed)
Chart: payload offset from the deck centre (m)
| 0.0 | 0.05 | 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.55 | 0.6 | 0.65 | 0.7 | 0.75 | 0.8 | 0.85 | 0.9 | 0.95 | 1.0 | 1.05 | 1.1 | 1.15 | 1.2
limit, 0° (between hubs) | 212.7137 | 197.8594 | 184.7741 | 173.9844 | 164.3125 | 155.7656 | 147.926 | 141.2656 | 134.8718 | 129.4062 | 124.2188 | 119.4688 | 114.9362 | 110.8828 | 107.2656 | 103.75 | 100.4688 | 97.3906 | 94.5156 | 91.7969 | 89.25 | 86.8438 | 84.5625 | 82.3906 | 80.3438
limit, 15° | 212.7137 | 194.7969 | 179.9375 | 167.3594 | 156.6406 | 147.375 | 138.9547 | 131.463 | 125.3906 | 119.625 | 114.375 | 109.4219 | 104.8694 | 100.9531 | 97.2031 | 93.75 | 90.5156 | 87.5469 | 84.7344 | 82.25 | 79.6406 | 77.3438 | 75.25 | 73.5 | 71.1562
limit, 30° | 212.7137 | 192.9688 | 176.8125 | 163.4844 | 152.2188 | 142.7656 | 133.8975 | 126.6406 | 119.8798 | 113.975 | 108.3478 | 103.9688 | 99.875 | 95.625 | 91.8281 | 88.4062 | 85.2344 | 82.2969 | 79.1656 | 76.9058 | 74.6094 | 72.3594 | 70.25 | 68.2656 | 66.3906
limit, 45° (towards a hub) | 212.7137 | 192.3125 | 175.8906 | 161.9869 | 150.7656 | 140.9688 | 132.4375 | 124.9531 | 118.3281 | 112.3906 | 106.9186 | 102.25 | 97.4217 | 93.8125 | 90.125 | 86.7188 | 83.5781 | 80.6562 | 77.9375 | 75.0924 | 72.9439 | 70.875 | 68.7344 | 66.9062 | 64.9062
45°, CG 0.5 m above the deck | 212.7137 | 174.6562 | 154.5 | 140.2969 | 129.3125 | 120.3906 | 112.8906 | 106.4844 | 100.8906 | 95.9531 | 91.5469 | 87.5938 | 83.9182 | 80.7344 | 77.7344 | 74.9844 | 72.4375 | 69.9926 | 67.8594 | 65.7969 | 63.9062 | 62.0625 | 60.3906 | 58.1216 | 57.5
45°, CG 1.0 m above the deck | 170.3594 | 138.9062 | 124.0781 | 113.6875 | 105.6406 | 99.0625 | 93.5156 | 88.7344 | 84.5469 | 80.8281 | 77.4844 | 74.4688 | 71.7188 | 69.2031 | 66.875 | 64.7344 | 62.7344 | 60.8906 | 59.1406 | 57.5156 | 55.9844 | 54.5469 | 53.1719 | 51.8906 | 50.6719
deck tilt 5° | 151.4169 | 105.8123 | 81.3198 | 66.0349 | 55.5864 | 47.9931 | 42.2247 | 37.6942 | 34.0419 | 31.0347 | 28.5154 | 26.3747 | 24.5329 | 22.9317 | 21.5264 | 20.2836 | 19.1764 | 18.1839 | 17.2889 | 16.4779 | 15.7397 | 15.065 | 14.4453
deck tilt 10° | 150.6708 | 123.9817 | 105.3245 | 91.5482 | 80.9591 | 72.5653 | 65.7487 | 60.1029 | 55.3497 | 51.2934 | 47.7911 | 44.7364 | 42.049 | 39.6657 | 37.5383 | 35.6275 | 33.902 | 32.3355 | 30.9078 | 29.6004 | 28.3993
deck tilt 20° | 121.6191 | 111.7572 | 103.3745 | 96.1619 | 89.89 | 84.3858 | 79.517 | 75.1796 | 71.2906 | 67.7844 | 64.6066 | 61.7136 | 59.069 | 56.6409 | 54.4049
Reading it
Below a solid line: stable and pins dry, for that direction.
Worst direction: towards a hub (red), by up to 19 %.
Every limit: one cluster's pins awash; the deck never tips with the mass on it.
Purple: CG 0.5 m and 1.0 m above the deck: lower limits, and a tip-over when centred at 1.0 m.
Dashed: deck tilt 5° (darkest), 10°, 20°.
Notes: The envelope. Each solid line is the payload limit for one direction of the offset, with the mass on the deck: every limit is a cluster's pins reaching the water. Towards a hub, on the diagonal (red), is the worst direction, by up to 19 percent. Purple: the worst direction with the CG raised half a metre and a metre. The grey dashed lines are deck tilts of 5, 10 and 20 degrees, far inside the limits.

## Slide 12
Mass and CG envelope of the whole platform
Total mass against the horizontal offset of the platform's CG (unloaded 358.3 kg, level geometry, payload on the deck)
Chart: horizontal offset of the platform's CG (mm)
| 0.0 | 17.78737075606229 | 34.022478354211785 | 49.02769444643396 | 62.87879150263331 | 75.7488720872131 | 87.66055990667786 | 98.96795719452496 | 109.38687778974338 | 119.39651085009265 | 128.71375614911756 | 137.5248213776486 | 145.7174742133827 | 153.6091077871436 | 161.2720270304737 | 168.39980955266518 | 175.18956164465672 | 181.65481932750635 | 187.8475495385329 | 193.7430833936186 | 199.4101481332529 | 204.83684374570035 | 210.03031278047794 | 214.99190937363943 | 219.7867956948802
limit, 0° (between hubs) | 571.0337 | 556.1794 | 543.0941 | 532.3044 | 522.6325 | 514.0856 | 506.246 | 499.5856 | 493.1918 | 487.7262 | 482.5387 | 477.7887 | 473.2562 | 469.2028 | 465.5856 | 462.07 | 458.7887 | 455.7106 | 452.8356 | 450.1169 | 447.57 | 445.1637 | 442.8825 | 440.7106 | 438.6637
limit, 45° (towards a hub) | 571.0337 | 550.6325 | 534.2106 | 520.3069 | 509.0856 | 499.2887 | 490.7575 | 483.2731 | 476.6481 | 470.7106 | 465.2386 | 460.57 | 455.7417 | 452.1325 | 448.445 | 445.0387 | 441.8981 | 438.9762 | 436.2575 | 433.4124 | 431.2639 | 429.195 | 427.0544 | 425.2262 | 423.2262
deck tilt 5° | 509.7369 | 464.1323 | 439.6398 | 424.3549 | 413.9064 | 406.3131 | 400.5447 | 396.0142 | 392.3619 | 389.3547 | 386.8354 | 384.6947 | 382.8529 | 381.2517 | 379.8464 | 378.6036 | 377.4964 | 376.5039 | 375.6089 | 374.7979 | 374.0597 | 373.385 | 372.7653
deck tilt 10° | 508.9908 | 482.3017 | 463.6445 | 449.8682 | 439.2791 | 430.8853 | 424.0687 | 418.4229 | 413.6697 | 409.6134 | 406.1111 | 403.0564 | 400.369 | 397.9857 | 395.8583 | 393.9475 | 392.222 | 390.6555 | 389.2278 | 387.9204 | 386.7193
deck tilt 20° | 479.9391 | 470.0772 | 461.6945 | 454.4819 | 448.21 | 442.7058 | 437.837 | 433.4996 | 429.6106 | 426.1044 | 422.9266 | 420.0336 | 417.389 | 414.9609 | 412.7249
At the limit
Payload at | Total mass | CG offset
0.0 m | 571 kg | 0 mm
0.2 m | 509 kg | 59 mm
0.4 m | 477 kg | 99 mm
0.6 m | 456 kg | 128 mm
0.8 m | 442 kg | 151 mm
1.0 m | 431 kg | 169 mm
1.2 m | 423 kg | 184 mm
Worst direction (towards a hub). The CG offset is that of the whole platform with the payload, before it tilts.
Notes: The same envelope as the whole platform's mass and centre of gravity. The platform weighs 358 kg unloaded. Its overall centre of gravity can move a few centimetres before the deck tilts 5 degrees, and roughly 15 to 20 centimetres before the limit, with the payload on the deck.

## Slide 13
Cluster and platform, side by side
Same buoys, same method; the platform spreads the buoys out and lifts the payload above the pins
 | Cluster (4 buoys) | Platform (16 buoys)
Unloaded mass | 88.1 kg | 358.3 kg
Centred limit (pins awash) | 54.7 kg | 212.7 kg
Sinkage per kg | 12.6 mm | 3.16 mm
Tilt stiffness | 67 N·m/rad (hub) | 1987 N·m/rad (deck)
Mass × offset for 5° of tilt | 0.60 kg·m | 15.1 kg·m
What limits off-centre loads | a pin awash; beyond ~0.3 m the hub rolls over | a cluster's pins awash, at every offset
Worst direction | towards a buoy | towards a hub (the diagonal)
Raised payload | not run (mass in the pin plane) | mass × CG height above the pins ≤ 202 kg·m
Buoys on their gimbals | never flop | never flop (margin ≥ 24 N·m/rad)
Notes: The cluster and the platform side by side. The platform carries about four clusters' worth centred, but it is thirty times stiffer in tilt, because its sixteen buoys work at about 0.8 m from the centre instead of 0.3 m. So off-centre loads that would roll a cluster's hub over only tilt the deck a few degrees. What the platform adds is height: its deck sits above the pins, so a raised payload can tip it, which the cluster with its mass in the pin plane never sees.

## Slide 14
Cross-checks
FloatSim's own platform model against the large-angle statics at small tilt
0.001°
largest tilt difference, like for like (every weight in the pin plane)
+1.6 %
more tilt with the real deck and payload heights: the weight on top FloatSim omits
Payload | Offset, direction | FloatSim sinkage / tilt | Statics, like for like | Statics, real heights
10 kg | 0.0 m, 0° | 79.0 mm / 0.000° | 79.0 mm / 0.000° | 79.0 mm / 0.000°
50 kg | 0.0 m, 0° | 210.6 mm / 0.000° | 210.6 mm / 0.000° | 210.6 mm / 0.000°
5 kg | 0.5 m, 0° | 62.5 mm / 0.736° | 62.5 mm / 0.736° | 62.5 mm / 0.744°
5 kg | 0.5 m, 45° | 62.5 mm / 0.736° | 62.5 mm / 0.736° | 62.5 mm / 0.744°
10 kg | 1.0 m, 0° | 79.0 mm / 2.946° | 79.0 mm / 2.947° | 79.0 mm / 2.992°
10 kg | 1.0 m, 30° | 79.0 mm / 2.946° | 79.0 mm / 2.947° | 79.0 mm / 2.992°
Both on FloatSim's 12-panel hydrostatics (C33 186.3 N/m per buoy). Sinkage is measured from the unloaded draft and includes the deck's and hubs' 14 kg.
Like for like: FloatSim's linear model has no weight term, so the statics put every weight in the pin plane too; then the two agree exactly.
Real heights: the deck 0.18 m above the pins and the payload on it. The extra tilt is the m g h effect FloatSim omits: small for these loads, but the effect that tips a raised payload.
Notes: How far to trust it. FloatSim, solving its own sixteen-buoy model of the platform with its joints, gives exactly the statics' sinkage and tilt when every weight is put in the pin plane, which is all FloatSim's linear model can represent. With the deck and payload at their real heights the statics tilt up to 1.6 percent more: that is the weight-on-top effect FloatSim leaves out, small for a payload on the deck, large for a raised one.

## Slide 15
What it means for loading the platform
Guidance
Keep the mass central and low. Centred on the deck: 213 kg before the pins are awash; it only sinks, 3.16 mm per kg.
Plan off-centre loads by deck tilt. 5° ↔ 15 kg·m, 10° ↔ 30 kg·m, in every direction.
Mind the payload's CG height. Mass × CG height above the pins must stay well below 202 kg·m: e.g. 150 kg with its CG no more than 1.2 m above the deck, as a stability limit.
Worst direction: towards a hub, by up to 19 % on the limit.
Not included
Waves and dynamics: calm-water statics; waves reduce the margins, most for raised payloads.
The mooring: free-floating; the mooring's lean and line loads are not included.
Payload shape: a point mass; a wide payload spreads its load, which the envelope treats as its CG.
Hardware: gimbal travel, the deck's own stiffness and payload retention are not modelled. The buoys never come close to touching (0.47 m between axes at worst).
Notes: What to take away. Keep heavy payloads low and central: then the platform carries about two hundred kilograms before its pins are awash. Plan off-centre loads by deck tilt. Watch the height of the payload's centre of gravity, which is the platform's new limit. The analysis is static and in calm water; waves, the mooring and the hardware would all reduce the margins.