## Slide 1
FLUME TEST ARTICLES · PAYLOAD SHIFT IN WAVES
Shifting the payload: what tilt does in waves
Cluster (12.5 kg) and platform (50 kg), level vs 5° vs 10° of tilt, regular waves H = 0.1 m, T = 1.5–5 s
Payload-stability study · 2026-10-18 · FloatSim with the weight preload, BEM re-run at each tilted equilibrium
Notes: This deck summarises what shifting a payload does to the cluster and the platform in waves. The payload is shifted until the hub or deck tilts 5 and 10 degrees, and both are run in six regular wave periods plus one at 4.2 s. All results are FloatSim, with the hydrodynamics recomputed at each tilted position and FloatSim's new weight preload switched on.

## Slide 2
The bottom line
H = 0.1 m regular waves along the shift; FloatSim with its weight preload
≈ 4.2 s
the buoys' rocking resonance with a payload (4.21 s cluster, 4.30 s platform)
11–12.6°
of rocking on the gimbals there, level or tilted
4.21 s
the cluster's rocking at 10° tilt, vs 4.22 s level: the tilt barely moves it
282 mm
lowest pin freeboard in the waves (platform, 10°): no pin awash
What the tilt does
Heave: the mass, not the tilt — the payload lengthens the heave period 2.59 → 2.71 s; tilt changes heave by ≤ 6 %.
Hub / deck tilting: near the article's heave and tilt resonance (2.6–2.9 s; the 2.65 s wave) the tilt turns heave into pitch: 2.2 → 3.8° on the cluster hub, 1.8 → 3.1° on the platform deck, level → 10°.
Freeboard: the tilt takes still-water freeboard from the low side; the waves take ~85–100 mm more at worst.
Buoys' own pitch: each buoy rocking on its gimbal — the flume record's 2.76–2.9 s pitch resonance — moves to ~4.2 s with a payload, whatever the tilt: keep a loaded article out of waves near 4.2 s.
Accelerations at the payload: vertical ≤ 0.04 g; lateral (along the waves) ≤ 0.8 m/s² from the waves, but a 10° tilt adds a constant 1.70 m/s² (0.17 g): up to 0.25 g in total.
Notes: Four numbers. With a payload on board, the buoys' rocking on their gimbals resonates at about 4.2 seconds, and there H = 0.1 m waves rock them 11 to 12.6 degrees. The tilt itself barely moves that resonance: the payload's mass sets it. And the pins stay well clear of the water at this wave height: the tightest case is the platform at 10 degrees, with 282 mm left.

## Slide 3
The cases
The payload centred, then shifted along the waves until the hub / deck tilts 5° and 10°
Cluster: 12.5 kg on the hub (50 kg / 4)
Platform: 50 kg on the deck
 | Cluster | Platform
Shift for 5° / 10° | 46 / 92 mm | 0.32 / 0.64 m
Lowest pin, still water: centred | 526 mm | 506 mm
… 5° | 500 mm | 437 mm
… 10° | 475 mm | 367 mm
Notes: The cases. On the cluster, 12.5 kg — a quarter of the platform's 50 kg — sits on the hub; on the platform 50 kg sits on the deck. Each is first centred, then shifted along the wave direction until the hub or deck tilts 5 and 10 degrees. The pictures are the solved static equilibria, to scale: the loaded side sinks, the other side rises, and the lowest pin loses freeboard. The unloaded article is run as well, for reference.

## Slide 4
How it was computed
Statics → hydrodynamics at the tilted geometry → FloatSim in waves
1 Static equilibrium
Large-angle statics: each buoy's draft, each pin's load, the payload offset for exactly 5° and 10°.
2 BEM at the tilt
Capytaine re-run with every buoy at its own position and draft, with its own hydrostatics (16 buoys: ~30 min a case).
3 FloatSim in waves
Regular waves H = 0.1 m along the shift, T = 1.5 / 2 / 2.35 / 2.65 / 3.5 / 4.2 / 5 s; drag relative to the waves.
4 Weight preload
FloatSim's new opt-in: the joints carry the static loads, so the load on each pin tips its buoy (see next slide).
Free-floating with a very soft horizontal hold (surge period ~45 s) against start-up drift; ~1 % effect on the wave response at 5 s, less below.
Checks: FloatSim's own static solve reproduces the statics geometry to 1e-15 m in all 8 cases; its natural periods match an independent closed-form estimate.
Notes: How it was computed. The large-angle statics give each case's equilibrium: where every buoy floats and how much load each pin carries. Capytaine recomputes the coupled hydrodynamics of the buoys at exactly those positions. FloatSim then runs regular waves about that equilibrium, with its new weight preload so the joints carry their static loads. A very soft horizontal hold stops the free article drifting; it barely touches the wave response.

## Slide 5
Why FloatSim's weight preload changes the answer
The load on each pin tips its buoy: it takes P × L off the buoy's righting stiffness
The buoy hangs from its pin, 1.62 m above its centre of gravity. The hub, deck and payload press down on the pin.
When the buoy leans, the pin and its load move sideways and push it further over: net righting = C55 − P × L.
FloatSim used to leave weights out of its statics, so the pins carried no load and the buoys looked too stiff.
With the preload, a payload slows the buoys' rocking from ~2.85 to ~4.2 s — into the wave band.
Case | Rocking period, no preload | With preload | Pin load | P·L / C55
Cluster, unloaded | 2.79 s | 2.95 s | 5 N | 8 / 75
Cluster, payload centred | 2.86 s | 4.22 s | 36 N | 58 / 106
Cluster, 10° tilt | 2.85 s | 4.21 s | 45 N | 73 / 117
Platform, unloaded | 2.81 s | 3.10 s | 9 N | 14 / 79
Platform, payload centred | 2.86 s | 4.38 s | 39 N | 64 / 110
Platform, 10° tilt | 2.85 s | 4.30 s | 65 N | 106 / 141
P·L / C55 in N·m/rad, the most loaded buoy. Heave, deck pitch and pin freeboard change little with the preload; the buoys' rocking changes completely.
Notes: Why the weight preload changes the answer. Each buoy hangs from its gimbal at the top of the spar, 1.6 m above its centre of gravity. The hub, deck and payload press down on that pin. When the buoy leans, the pin moves sideways and the load on it pushes the buoy further over: it takes P times L off the buoy's righting stiffness. FloatSim used to leave the weights out of its statics, so the pins carried nothing and the buoys looked far too stiff. With the preload, a payload slows the buoys' rocking from about 2.85 to about 4.2 seconds.

## Slide 6
Heave: the payload's mass matters, the tilt hardly does
Heave of the hub / deck centre against wave period
Chart: Cluster, 12.5 kg on the hub
| 1.5 | 2.0 | 2.35 | 2.65 | 3.5 | 4.2 | 5.0
unloaded | 1.8452 | 15.9447 | 46.2908 | 74.9825 | 65.0366 | 56.3505 | 53.08
payload centred | 1.1927 | 11.0736 | 36.2152 | 67.8572 | 69.2954 | 58.3553 | 53.6248
shifted: 5° tilt | 1.1881 | 11.0426 | 35.8406 | 67.2107 | 69.2576 | 58.3726 | 53.6258
shifted: 10° tilt | 1.1636 | 11.0186 | 35.3721 | 66.2049 | 69.2201 | 58.4723 | 53.6304
Chart: Platform, 50 kg on the deck
| 1.5 | 2.0 | 2.35 | 2.65 | 3.5 | 4.2 | 5.0
unloaded | 0.24654 | 10.6339 | 37.7668 | 65.7606 | 62.8881 | 55.4523 | 52.6481
payload centred | 0.15584 | 7.3895 | 29.6063 | 60.3325 | 67.1786 | 56.6628 | 53.1929
shifted: 5° tilt | 0.18395 | 7.1637 | 27.5342 | 55.8723 | 66.8807 | 56.6819 | 53.205
shifted: 10° tilt | 0.34723 | 7.0921 | 25.7472 | 49.5144 | 66.4198 | 57.2031 | 53.2481
The payload lengthens the heave period (2.59 → 2.71 s cluster, 2.60 → 2.72 s platform), so heave falls a little below resonance. 5° and 10° of tilt change heave by ≤ 6 %.
Notes: The payload lengthens the heave period (2.59 → 2.71 s cluster, 2.60 → 2.72 s platform), so heave falls a little below resonance. 5° and 10° of tilt change heave by ≤ 6 %.

## Slide 7
Near the heave resonance, the tilt turns heave into pitch
Hub / deck pitch (the whole article tilting; not the buoys' own pitch) — resonates with heave at 2.6–2.9 s
Chart: Cluster, 12.5 kg on the hub
| 1.5 | 2.0 | 2.35 | 2.65 | 3.5 | 4.2 | 5.0
unloaded | 0.19541 | 0.91594 | 1.9714 | 2.5387 | 1.2411 | 0.7409 | 0.49159
payload centred | 0.14472 | 0.77193 | 1.71 | 2.1524 | 1.1744 | 0.71646 | 0.47831
shifted: 5° tilt | 0.22357 | 0.84749 | 2.1544 | 2.9095 | 1.3376 | 0.7685 | 0.46772
shifted: 10° tilt | 0.35827 | 0.96591 | 2.6855 | 3.8045 | 1.6228 | 1.0207 | 0.43149
Chart: Platform, 50 kg on the deck
| 1.5 | 2.0 | 2.35 | 2.65 | 3.5 | 4.2 | 5.0
unloaded | 0.10433 | 0.71493 | 1.7118 | 2.2943 | 1.2492 | 0.74206 | 0.49334
payload centred | 0.066665 | 0.45946 | 1.2341 | 1.8245 | 1.0994 | 0.52802 | 0.52004
shifted: 5° tilt | 0.11695 | 0.51327 | 1.516 | 2.4821 | 1.3097 | 0.63803 | 0.5081
shifted: 10° tilt | 0.17987 | 0.56409 | 1.718 | 3.069 | 1.715 | 1.0294 | 0.47646
At 2.65 s the cluster hub pitches 2.2 → 2.9 → 3.8° and the platform deck 1.8 → 2.5 → 3.1° (level → 5° → 10°): the shifted mass couples the article's heave and pitch, which resonate together at 2.6–2.9 s. Away from it, including at the buoys' rocking resonance (4.2 s), the tilt adds almost no pitch.
Notes: At 2.65 s the cluster hub pitches 2.2 → 2.9 → 3.8° and the platform deck 1.8 → 2.5 → 3.1° (level → 5° → 10°): the shifted mass couples the article's heave and pitch, which resonate together at 2.6–2.9 s. Away from it, including at the buoys' rocking resonance (4.2 s), the tilt adds almost no pitch.

## Slide 8
The tilt costs freeboard; the waves take a little more
Smallest pin freeboard during the wave cycle
Chart: Cluster, 12.5 kg on the hub
| 1.5 | 2.0 | 2.35 | 2.65 | 3.5 | 4.2 | 5.0
unloaded | 638.3742 | 624.9629 | 606.3775 | 604.3098 | 673.6425 | 684.0461 | 687.4383
payload centred | 474.6552 | 464.7454 | 446.2498 | 444.4346 | 503.3184 | 485.2621 | 521.9979
shifted: 5° tilt | 448.4012 | 438.9027 | 420.3279 | 416.8519 | 476.5927 | 460.3858 | 496.2208
shifted: 10° tilt | 422.3208 | 413.2358 | 394.7303 | 389.4642 | 449.668 | 435.0892 | 470.5724
Chart: Platform, 50 kg on the deck
| 1.5 | 2.0 | 2.35 | 2.65 | 3.5 | 4.2 | 5.0
unloaded | 618.9471 | 605.6918 | 587.6663 | 592.2879 | 651.8788 | 664.0659 | 667.5991
payload centred | 455.0567 | 445.1534 | 426.5686 | 424.1597 | 483.3457 | 470.5176 | 501.3782
shifted: 5° tilt | 384.6421 | 376.1058 | 358.1367 | 353.9311 | 411.0256 | 405.7895 | 431.8902
shifted: 10° tilt | 314.9815 | 307.2331 | 291.0009 | 282.3733 | 336.4854 | 332.0166 | 362.5109
The lowest pins lose still-water freeboard as the article tilts; the waves take ~85 mm more at worst (2.65 s). No pin comes near the water at H = 0.1 m; linearly, at 10° a pin would reach it only at H ≈ 0.43 m (platform) or 0.56 m (cluster).
Notes: The lowest pins lose still-water freeboard as the article tilts; the waves take ~85 mm more at worst (2.65 s). No pin comes near the water at H = 0.1 m; linearly, at 10° a pin would reach it only at H ≈ 0.43 m (platform) or 0.56 m (cluster).

## Slide 9
With a payload, the buoys rock hard at ~4.2 s
The buoys' own pitch on their gimbals (dashed: FloatSim without the weight preload, payload centred)
Chart: Cluster, 12.5 kg on the hub
| 1.5 | 2.0 | 2.35 | 2.65 | 3.5 | 4.2 | 5.0
unloaded | 1.2314 | 1.723 | 3.7079 | 8.1983 | 2.1364 | 0.66411 | 0.30998
payload centred | 0.72125 | 0.65626 | 1.7788 | 3.0465 | 4.0556 | 12.3289 | 1.4709
shifted: 5° tilt | 0.79909 | 0.69354 | 1.9818 | 3.6381 | 4.2351 | 12.3264 | 1.4995
shifted: 10° tilt | 0.88204 | 0.72319 | 2.2851 | 4.3304 | 4.5422 | 12.6075 | 1.5556
payload centred (without preload) | 0.87579 | 1.0831 | 2.5143 | 6.9286 | 0.54749 | 0.17859 | 0.21117
Chart: Platform, 50 kg on the deck
| 1.5 | 2.0 | 2.35 | 2.65 | 3.5 | 4.2 | 5.0
unloaded | 0.84103 | 2.1425 | 4.0447 | 6.6175 | 3.2273 | 0.87541 | 0.50408
payload centred | 0.70872 | 1.6129 | 2.8 | 3.6107 | 3.4944 | 11.0638 | 1.9605
shifted: 5° tilt | 0.83811 | 1.8349 | 3.0801 | 3.8136 | 3.5059 | 11.2318 | 1.9687
shifted: 10° tilt | 0.96988 | 2.0461 | 3.2933 | 3.8071 | 3.4655 | 11.1928 | 1.8073
payload centred (without preload) | 0.74297 | 1.8247 | 3.5276 | 7.2084 | 0.61937 | 0.6055 | 0.85304
With the preload, a payload puts the buoys' rocking resonance at ~4.2 s, where they rock 11–12.6° — level or tilted. Without the preload FloatSim gave ≤ 0.7° there and a peak at 2.65 s — the flume record's 2.76–2.9 s pitch resonance, which leaves out the load on the pins.
Notes: With the preload, a payload puts the buoys' rocking resonance at ~4.2 s, where they rock 11–12.6° — level or tilted. Without the preload FloatSim gave ≤ 0.7° there and a peak at 2.65 s — the flume record's 2.76–2.9 s pitch resonance, which leaves out the load on the pins.

## Slide 10
Watch it move: 2.65 s, the heave and pitch resonance
Payload shifted to 10°, H = 0.1 m · FloatSim with its weight preload · true scale, real time · plays in slide show
The whole article heaves and pitches about its tilt: hub ±3.8°, deck ±3.1°; heave 66 / 50 mm. The buoys hang nearly straight (±4.3° / ±3.8°); the lowest pin keeps 389 / 282 mm.
Notes: At 2.65 s the whole article heaves and pitches about its 10 degree tilt. The buoys hang nearly straight below their pins: this is the resonance of the article as a whole, where the tilted payload turns heave into pitch and the lowest pins come closest to the water. True scale, real time; the animations play in slide show.

## Slide 11
Watch it move: 4.2 s, the buoys' rocking resonance
Payload shifted to 10°, H = 0.1 m · FloatSim with its weight preload · true scale, real time · plays in slide show
The buoys swing together on their pins (±12.6° cluster, ±11.2° platform) while the hub / deck slides along the waves (0.48 / 0.41 m/s² lateral at the payload); the article barely pitches (±1.0° / ±1.0°).
Notes: At 4.2 s the article as a whole barely pitches, but the buoys swing together on their pins while the hub or deck slides back and forth along the waves on top of them. This is the loaded buoys' rocking resonance, the one the weight preload revealed. True scale, real time; the animations play in slide show.

## Slide 12
Accelerations at the payload: vertical is small
Vertical acceleration amplitude at the payload against wave period, H = 0.1 m (1 g = 9.81 m/s²)
Chart: Cluster, 12.5 kg on the hub
| 1.5 | 2.0 | 2.35 | 2.65 | 3.5 | 4.2 | 5.0
unloaded | 0.032377 | 0.15738 | 0.33068 | 0.4241 | 0.20921 | 0.12611 | 0.083812
payload centred | 0.020931 | 0.10931 | 0.25888 | 0.38152 | 0.22301 | 0.13077 | 0.084665
shifted: 5° tilt | 0.02291 | 0.10948 | 0.25668 | 0.37923 | 0.22338 | 0.13122 | 0.084694
shifted: 10° tilt | 0.028475 | 0.11013 | 0.25179 | 0.37426 | 0.22456 | 0.13356 | 0.084794
Chart: Platform, 50 kg on the deck
| 1.5 | 2.0 | 2.35 | 2.65 | 3.5 | 4.2 | 5.0
unloaded | 0.0043271 | 0.10497 | 0.26997 | 0.37065 | 0.20211 | 0.1241 | 0.083133
payload centred | 0.0027352 | 0.072943 | 0.21167 | 0.33921 | 0.21638 | 0.1259 | 0.083969
shifted: 5° tilt | 0.011683 | 0.077428 | 0.2007 | 0.32222 | 0.22051 | 0.12568 | 0.084296
shifted: 10° tilt | 0.032728 | 0.089636 | 0.18939 | 0.30201 | 0.23546 | 0.13781 | 0.085445
At most 0.42 m/s² (0.04 g), unloaded, near the heave resonance; with the payload 0.38 (cluster) and 0.34 m/s² (platform). Both articles ride the same buoys' heave, so they are alike, and the tilt changes it little.
Notes: Accelerations at the payload, where it sits in each case. Vertical first: small on both articles, at most about four hundredths of g, peaking near the heave resonance around 2.65 s. The payload's mass lowers them a little and the tilt hardly changes them.

## Slide 13
Lateral acceleration (along the waves)
As the payload feels it: the deck's motion plus gravity swinging along the deck as it pitches
Chart: Cluster, 12.5 kg on the hub
| 1.5 | 2.0 | 2.35 | 2.65 | 3.5 | 4.2 | 5.0
unloaded | 0.94858 | 0.98844 | 1.0544 | 1.1597 | 0.34581 | 0.10719 | 0.04426
payload centred | 0.6295 | 0.61757 | 0.61067 | 0.43227 | 0.13111 | 0.60094 | 0.078906
shifted: 5° tilt | 0.63195 | 0.62802 | 0.69263 | 0.53992 | 0.10034 | 0.56326 | 0.076516
shifted: 10° tilt | 0.6393 | 0.64596 | 0.78692 | 0.68019 | 0.056404 | 0.47621 | 0.068956
Chart: Platform, 50 kg on the deck
| 1.5 | 2.0 | 2.35 | 2.65 | 3.5 | 4.2 | 5.0
unloaded | 0.12211 | 0.63106 | 0.78852 | 0.73632 | 0.43767 | 0.12132 | 0.04937
payload centred | 0.080471 | 0.39475 | 0.48526 | 0.39799 | 0.090937 | 0.51814 | 0.10382
shifted: 5° tilt | 0.086935 | 0.39778 | 0.5317 | 0.49014 | 0.048675 | 0.49403 | 0.097211
shifted: 10° tilt | 0.10986 | 0.40474 | 0.56832 | 0.59826 | 0.046398 | 0.41077 | 0.079972
Short waves: the platform's 2.4 m span averages them out: 0.08 against 0.63 m/s² at 1.5 s (payload centred).
Near the heave resonance (2.35–2.65 s): the tilt adds lateral load: cluster 0.61 → 0.79, platform 0.49 → 0.60 m/s², level → 10°.
At 4.2 s, with a payload: 0.4–0.6 m/s²: the buoys rocking on their gimbals slide the hub / deck along the waves.
Notes: Lateral acceleration, horizontal along the waves, as the payload feels it: the deck's motion plus gravity swinging along the deck as it pitches. The platform is much calmer in short waves because its 2.4 m span averages them out. Near the heave resonance the tilt adds lateral load through the coupled pitch. And at 4.2 s, with a payload, both feel about half a metre per second squared: the buoys rocking on their gimbals make the hub or deck slide along the waves.

## Slide 14
For the payload, the static tilt is the biggest lateral load
Maximum accelerations at the payload over the seven wave periods, m/s² (H = 0.1 m)
 | Vertical, max | Lateral from the waves, max | Static tilt, g·sin θ | Total lateral, max
Cluster, unloaded | 0.42 | 1.16 | 0.00 | 1.16 (0.12 g)
Cluster, payload centred | 0.38 | 0.63 | 0.00 | 0.63 (0.06 g)
Cluster, 5° tilt | 0.38 | 0.69 | 0.85 | 1.55 (0.16 g)
Cluster, 10° tilt | 0.37 | 0.79 | 1.70 | 2.49 (0.25 g)
Platform, unloaded | 0.37 | 0.79 | 0.00 | 0.79 (0.08 g)
Platform, payload centred | 0.34 | 0.52 | 0.00 | 0.52 (0.05 g)
Platform, 5° tilt | 0.32 | 0.53 | 0.85 | 1.39 (0.14 g)
Platform, 10° tilt | 0.30 | 0.60 | 1.70 | 2.30 (0.23 g)
1.70 m/s²
along the deck from a 10° tilt alone (0.17 g), before any wave
0.25 / 0.23 g
worst total lateral at 10°: cluster / platform
Keeping the payload level matters more for its lateral restraint than the wave motion does.
Notes: For the payload's lateral restraint, the static tilt is the biggest load. Tilted 10 degrees, the payload feels a constant 1.7 metres per second squared along the deck from gravity alone, about 0.17 g, before any wave. The waves add at most about 0.8 on top, for a total of about a quarter of g at H = 0.1 m.

## Slide 15
One rocking period for all the buoys
Each buoy alone would differ; tied to one hub they rock together
Cluster at 10° | Sinkage | Load on pin | Net stiffness | Period if alone
Loaded pair | 242 mm | 45 N | 44 N·m/rad | ~4.44 s
Other pair | 140 mm | 26 N | 54 N·m/rad | ~4.01 s
Level (all four) | 191 mm | 36 N | 49 N·m/rad | 4.22 s
The hub carries all the pins together: in the mode the waves drive, every buoy leans the same way, so they share one period.
Its stiffness is the sum of theirs: 2 × 44 + 2 × 54 = 196, against 4 × 49 = 195 level → 4.21 vs 4.22 s.
Why: a buoy's stiffness falls almost linearly as it sinks; the shift sinks one side and lifts the other by the same amount.
12.4–12.6°
the four cluster buoys' rocking at 4.2 s, 10° tilt: almost equal
10.1–11.2°
all 16 platform buoys at 4.2 s, 10° tilt
The buoys can rock against each other only by sliding sideways relative to one another — those modes sit near 9 s. A cross-wise twisting pair (3.7 / 4.4 s) needs waves from the side to be driven.
Notes: Wouldn't each buoy rock at its own period once the load is shifted? On its own, yes: at 10 degrees the cluster's loaded pair is softer and would rock at about 4.45 seconds, the other pair at about 4.0. But they all hang from the same hub. In the mode the waves drive, every buoy leans the same way while the hub slides under them, so they rock together at one period, set by the sum of their stiffnesses. Shifting the payload softens one side and stiffens the other by almost the same amount, so the sum, and the period, hardly change.

## Slide 16
What it means for testing with a payload
Guidance
Avoid waves near 4.2 s with a payload on board: the buoys rock 11–12.6° on their gimbals at H = 0.1 m, level or tilted.
The mass sets the rocking; the tilt sets the freeboard: keep the payload level to keep the low side's pins dry.
Near the heave resonance (2.6–2.8 s) a tilted payload adds pitch: up to 3.8° (cluster) and 3.1° (platform) at 10°.
Pins stay dry at H = 0.1 m in every case (≥ 282 mm).
Lateral restraint: design for the static tilt plus waves: up to 0.25 g at 10°, of which 0.17 g is the tilt alone.
Not included
Large rocking: 11–12.6° is past FloatSim's small-angle range (5.7°); the size is indicative, the resonance period is not. Gimbal travel is not modelled.
Waves: regular, along the shift only; waves from the side drive other modes.
Periods: seven points; the peaks between them are not resolved.
Model: linear about each equilibrium; 12-panel BEM (~0.05 s on the periods); free-floating with a soft hold, not the flume mooring.
Notes: What to take away. With a payload on board, the period to watch is about 4.2 seconds, where the buoys rock hard on their gimbals, and that holds whether the payload is level or not. The tilt itself matters for freeboard and for pitch near the heave resonance. The analysis is linear and in regular waves along the shift; the large rocking angles are past FloatSim's small-angle range, so their size is indicative.

## Slide 17
Appendix: FloatSim's weight preload
Opt-in `simulation.weight_preload: true` (main 05128b7, dd889f2; docs/weight-preload-plan.md)
Check | Result
Gate A: a float pinned at its top, T = 2π√((I + mL²)/(C55 − P L)) | pin force exact; periods within 1e-4 (9.98 / 4.62 / 5.93 s); finite-amplitude correction matches
Gate B: switch off | unchanged: 786 fast tests pass
Gate C: the flume cluster vs the study's statics | 157.94 mm sinkage (10 kg), 0.869° tilt (1 kg at 0.1 m), a quarter of the load per pin
Geometric stiffness K_geo | = the closed form (−P L) on the pinned float and on the cluster; symmetric
This study | static solve keeps the statics geometry to 1e-15 m; periods = the closed-form estimate
The flume mooring and wall-effect records were run without the preload: their buoy-rocking results are the ones affected (the unloaded platform's rocking mode is 3.10 s, not 2.81 s).
Notes: For reference: the FloatSim change behind these results. The weight preload is opt-in. It adds every body's weight and each floating body's buoyancy, solves the static equilibrium through the joints, carries the joint loads in the dynamics, and refuses any model whose loads leave it without restoring. It was validated against a closed-form pinned float, against the full test suite with the switch off, and against this study's hand statics on the real cluster.

## Slide 18
Appendix: what loading each buoy does
Its share of the hub, deck and payload sits on its pin, 1.62 m above its centre of gravity
Chart: One buoy, loaded on its pin (12-panel table)
| 0.0 | 0.025 | 0.05 | 0.075 | 0.1 | 0.125 | 0.15 | 0.175 | 0.2 | 0.225 | 0.25 | 0.275 | 0.3 | 0.325 | 0.35 | 0.375 | 0.4 | 0.425 | 0.45 | 0.475 | 0.5 | 0.525 | 0.55 | 0.575 | 0.6 | 0.625 | 0.65 | 0.675 | 0.7 | 0.71 | 0.715
buoy's own righting, C55 | 70.7711 | 75.0527 | 79.4507 | 83.9652 | 88.596 | 93.3433 | 98.2069 | 103.187 | 108.2835 | 113.4964 | 118.8257 | 124.2714 | 129.8336 | 135.5121 | 141.3071 | 147.2184 | 153.2462 | 159.3904 | 165.651 | 172.028 | 178.5214 | 185.1313 | 191.8575 | 198.7002 | 205.6592 | 212.7347 | 219.9266 | 227.2349 | 234.6596 | 237.6621 | 239.1703
tipping by the pin load, P × L | 0 | 7.5621 | 15.1242 | 22.6862 | 30.2483 | 37.8104 | 45.3725 | 52.9346 | 60.4966 | 68.0587 | 75.6208 | 83.1829 | 90.745 | 98.307 | 105.8691 | 113.4312 | 120.9933 | 128.5554 | 136.1174 | 143.6795 | 151.2416 | 158.8037 | 166.3658 | 173.9278 | 181.4899 | 189.052 | 196.6141 | 204.1762 | 211.7382 | 214.7631 | 216.2755
net rocking stiffness | 70.7711 | 67.4906 | 64.3266 | 61.2789 | 58.3477 | 55.5329 | 52.8345 | 50.2524 | 47.7869 | 45.4377 | 43.2049 | 41.0885 | 39.0886 | 37.2051 | 35.4379 | 33.7872 | 32.2529 | 30.835 | 29.5336 | 28.3485 | 27.2798 | 26.3276 | 25.4918 | 24.7723 | 24.1693 | 23.6827 | 23.3125 | 23.0588 | 22.9214 | 22.899 | 22.8949
It sinks to carry its load: P = C33 × sinkage, 186 N per metre, until the spar top (the pin) reaches the water.
Sinking raises its righting: the new buoyancy is added high up the spar: C55 grows 71 → 239 N·m/rad by the time the pin reaches the water.
The load on the pin tips it: when the buoy leans, the pin and its load move sideways and push it over: P × L grows 0 → 216 N·m/rad.
Net: the more load, the softer it rocks: 71 → 23 N·m/rad. A payload slows the buoys' rocking from ~2.85 to ~4.2 s.
A shifted payload loads the near buoys more: they sink deeper, lose freeboard and get softer; the far ones rise and stiffen. All the buoys still rock together at one period (the sum of their stiffnesses barely changes).
Buoy | Cluster: sinkage | P·L / C55 | Net | Pin above water | Platform: sinkage | P·L / C55 | Net | Pin above water
unloaded | 26 mm | 8 / 75 | 67 | 691 mm | 46 mm | 14 / 79 | 65 | 671 mm
payload centred | 191 mm | 58 / 106 | 49 | 526 mm | 211 mm | 64 / 110 | 47 | 506 mm
10° tilt, loaded side | 242 mm | 73 / 117 | 44 | 475 mm | 350 mm | 106 / 141 | 35 | 367 mm
10° tilt, other side | 140 mm | 42 / 96 | 54 | 577 mm | 72 mm | 22 / 83 | 62 | 645 mm
Notes: What loading a buoy does. Each buoy carries its share of the hub, deck and payload on its pin, and sinks until the extra buoyancy carries it. Sinking raises the buoy's own righting, because the new buoyancy is added high up the spar. But the load sits on the pin 1.62 m above the buoy's centre of gravity, and when the buoy leans that load pushes it further over: P times L. That grows faster than the righting, so the net rocking stiffness falls as the buoy is loaded. Shifting the payload loads the near buoys more and the far ones less: the near side sinks deeper, loses freeboard and gets softer; the far side the opposite.

## Slide 19
Appendix: FloatSim's small-rotation limit at the pins
Linear about each equilibrium: rotations, including each buoy's rotation on its pin, must stay below ~0.1 rad (5.7°)
Motion | Largest here | Within ~5.7°?
Static tilt of the hub / deck (5°, 10°) | 10° | not needed: each case is built about its own tilted equilibrium (BEM re-run there)
Hub / deck pitch in the waves | 3.8° | yes
Pin motion relative to the water | 84 mm | yes (small against the spar)
Buoys rocking on their pins (gimbals), 4.2 s | 12.6° | no: ~2.2× the limit
What FloatSim linearises: the rotations (small-angle, rotation vector); the hydrostatic restoring (a fixed matrix at the BEM draft); the wave forces (at the mean position); the pin load's tipping (P L θ, not P L sin θ); the gimbals' yaw lock (first order in the relative angle).
What it keeps exact: where the pins are (the joint arms rotate with the bodies) and the drag (non-linear, relative to the waves).
At 12.6° of rocking
Geometry: small error. sin θ / θ = 0.992; the pin drops L(1 − cos θ) = 39 mm, which the exact pin positions already carry.
Damping: the real uncertainty. The amplitude at resonance is set by the drag and the perforated heave plate, whose damping is still to be measured in the tank.
Not modelled: the gimbals' travel and any stops; a non-linear (Level 2) FloatSim, tracked as LEVEL2-INTEGRATOR-UNWIRED.
So: the resonance period (~4.2 s) stands; read the 11–12.6° as indicative, and confirm with a rocking decay in the tank.
Notes: FloatSim's small-rotation limit, and where it bites in this study. FloatSim is linear about the equilibrium: it treats rotations, including each buoy's rotation on its pin, as small, up to about a tenth of a radian. The static tilts of 5 and 10 degrees are not a problem, because every case was built about its own tilted equilibrium, with the hydrodynamics recomputed there. The wave motions on top must be small: the deck and hub pitch, at most about 4 degrees, are. The buoys' rocking on their pins at 4.2 seconds, 11 to 12.6 degrees, is about twice the limit. The geometry error there is small; the real uncertainty is the damping that sets the amplitude. So that amplitude is indicative, while the resonance period stands.